## Slide 1
Ionization Charge Unfolding at Zero-Suppressed Liquid Argon Time Projection Chamber
An Author | Brookhaven National Laboratory
JINST paper proposal • Signal Processing for ND-LAr

## Slide 2
Paper at a Glance
Structure overview
1. Introduction
ND-LAr physics motivation, zero-suppression challenge
2. Signal Processing
Traditional deconvolution review, readout logic, algorithm
3. Performance
Simulation setup, template/filter/threshold/noise studies
4. Discussion
Truth bookkeeping, hardware, readout requirements, shield grid
5. Summary
Conclusions and outlook

## Slide 3
Motivation
Why zero suppression breaks conventional signal processing
Introduction
ND-LAr facts
• Pixelated readout (LArPix-v2 ASICs)
• Self-triggering: electronics dormant until charge exceeds discriminator threshold
• ADC fires only after a configurable hold delay (adc_hold_delay)
• Front-end resets and drains charge after each burst sequence
• Burst mode: records several consecutive integration windows without reset
Consequences for signal processing
• Waveform is truncated: only charge above threshold is recorded
• First trigger time is known; subsequent hits lose exact start time
• Negative induction signals from neighboring pixels are never recorded
• Reset mechanism may cause charge to be lost or overestimated
• Traditional deconvolution assumes full, equally-spaced waveform sampling
Goal: Recover approximate full waveforms using physics-guided templates, then apply FFT-based 3D deconvolution to unfold the ionization charge.

## Slide 4
Traditional Signal Processing
What works at the far detector
Section 2 review
System model: m(t) = r(t) * s(t) + n(t)
• m(t) measured waveform, r(t) detector + electronics response, s(t) ionization signal, n(t) noise
• Deconvolution in frequency domain: S(w) = M(w) / R(w) (minus noise term)
• Gaussian filter suppresses blow-up at small R(w) while preserving the charge integral
• Region-of-interest (ROI) selection removes signal-free time bins
• Wiener-inspired filters give simultaneous spatial and charge resolution
Why this fails at ND-LAr
• Zero suppression destroys the continuous, equally-spaced waveform required by FFT
• The recorded signal is no longer a linear function of ionization charge
• Direct convolution / deconvolution on raw measurements is invalid

## Slide 5
ND-LAr Readout Logic
Self-triggering and burst mode details
Section 2 — readout review
Self-trigger cycle (single hit)
• Charge accumulates on CSA front-end
• Discriminator fires when charge > threshold
• After adc_hold_delay, ADC latches charge if still above threshold (veto random noise)
• During ADC conversion, no new triggers possible => dead time
• Front-end resets; new charge accumulation starts
• First trigger time is recorded precisely; consecutive hits lose exact start time
Burst mode extension
• Front-end does NOT reset after the first hold window
• Records several more charge integrals at fixed time windows (adc_hold_delay)
• Resets only at the end of the burst sequence
• Burst length (nburst) is a configurable parameter
• Gives more waveform samples per trigger at the cost of saturation risk
• Code: t_first = trigger_time + adc_hold_delay; t_last = trigger_time + adc_hold_delay * nburst
Key quantity: the gap between two burst sequences = t_B_start - t_A_last (difference of burst start times, not integration end times)

## Slide 6
Algorithm Overview
Three-stage pipeline
Section 2 — algorithm
Stage 1 Waveform Recovery
Stage 2 3D FFT Deconvolution
Stage 3 Active Voxel Selection
• Extract burst sequences per pixel
• Pass 1: dead-time merge (gap <= tau)
• Pass 2: template compensation (gap > tau)
• Assemble into 3D block
• Load & integrate field response kernel
• Build 3D Gaussian filter
• FFT deconvolution: S = M / R x G
• Trim & roll output to correct offset
• Apply 3D Gaussian filter to deconv output
• Select voxels with charge > 500 e-
• (Ongoing) Wiener-inspired frequency filter
• Compare with smeared truth for residual
Input: raw LArPix hit data (pixel x/y, trigger time, burst charge integrals) Output: 3D deconvolved charge image

## Slide 7
Stage 1 — Burst Sequence Extraction
From raw hits to per-pixel sequences
Algorithm detail
Raw hit data format (Hits container)
location[:, 0] pixel_x location[:, 1] pixel_y location[:, 2] trigger_time_idx location[:, 3] last_adc_latch location[:, 4] next_integration_start data[:, 3:] cumulative charge per burst window
Per-pixel BurstSequence construction
• charges = diff(cumulative data) => charge per burst window
• t_first = trigger_time_idx + adc_hold_delay
• t_last = trigger_time_idx + adc_hold_delay * nburst
• Sequences grouped by (pixel_x, pixel_y) and sorted by trigger_time_idx
• Validation: no overlapping sequences (t_first[k+1] >= t_last[k])
Gap definition
gap = seq_B.t_first - seq_A.t_last (gap between the start of B and the start of the last burst of A, NOT the end of A's integration window)
• gap = 0: sequences are adjacent (touching) but not overlapping
• 0 < gap <= tau: close enough for dead-time compensation (Pass 1)
• gap > tau: template compensation required (Pass 2)

## Slide 8
Stage 1 — Two-Pass Waveform Recovery
Dead-time merge then template fill
Algorithm detail (BurstSequenceProcessorV3)
Pass 1 — Dead-Time Compensation
• Iterate over sequences for a pixel in time order
• If gap <= tau: merge seq_A and seq_B
• slope = charge_B[0] / (gap - deadtime)
• compensated = slope * deadtime
• first charge of B += compensated
• Output: list of MergedBurstGroups (one per cluster)
Pass 2 — Template Compensation
• Treat each MergedBurstGroup as a block
• Select template: collection (max cumq > threshold) or
• induction positive prefix (max cumq <= threshold)
• Find transit fraction: threshold / max_cumulative_charge
• Scan template to find window of length = gap - deadtime
• that rises by transit fraction
• Interpolate template points, append before group
• Scale so template endpoint equals threshold
• Output: continuous MergedSequence per pixel
Bootstrap (first sequence): no previous time; scan template from its start to find where cumulative equals transit fraction, then work backwards to trigger_time_idx.
Block assembly
• All MergedSequences binned into 3D array (pixel_x, pixel_y, time_bin)
• Time bin size = adc_hold_delay; padded by npadbin bins on each side

## Slide 9
Burst Processor Versions
V1 vs V2 vs V3 strategies
Algorithm variants (burst_processor.py / v2.py / v3.py)
Aspect
V1
V2
V3
Passes
Single pass
Single pass
Two passes
Dead-time merge
Slope compensation
Slope compensation
Pass 1 only
Time alignment
Global binning only
Fractional FFT phase shift
Global binning only
Template mode
Single (cumulative)
Single (cumulative)
Dual: collection + induction
Template selection
Fixed per pixel
Fixed per pixel
Per merged group by charge
Notes:
• V1: baseline single-pass processor; most direct implementation of dead-time + template compensation.
• V2: adds sub-sample time-jitter correction via frequency-domain phase shifts; higher complexity; not used in current pipeline.
• V3 (current): two-pass strategy separates close-sequence merging from distant-gap filling; introduces charge-dependent template selection.

## Slide 10
Stage 1 — Field Response Templates
What gets used as the physics template
Algorithm detail (deconv_workflow.py / field_response.py)
Three template modes
center
Response at the center of the collection pixel only. Fast, symmetric, good approximation for high-charge pixels.
collection
Average response over all intra-pixel sampling paths of the collection pixel. Reduces path-dependent smearing.
collection_plus_neighbors
Average over collection pixel plus the 8 surrounding neighbors (radius=1). Captures long-range induction; uses positive_cumulative template search mode. V3 processor further splits: collection template for pixels with max cumq > threshold, induction (positive-prefix only) for pixels with max cumq <= threshold.
Template preprocessing
• Raw field response multiplied by time_tick, spatial quadrant mirrored to full plane
• Kernel flipped for convolution; intra-pixel paths downsampled by averaging
• Cumulative template built from cumsum, then maximum.accumulate enforces monotone increase (handles bipolar dips)
• Induction template for V3: keep only leading positive prefix of bipolar waveform

## Slide 11
Stage 2 — 3D FFT Deconvolution
Inverting the detector response in frequency space
Algorithm detail (deconv.py)
Inputs
• Recovered 3D charge block (pixel_x, pixel_y, time_bin)
• Field response kernel: averaged over intra-pixel paths, then summed per adc_hold_delay time window
• kernel shape: (n_pix_x, n_pix_y, n_time_bins)
• 3D Gaussian filter sigma_pixel x sigma_pixel x sigma_time
Deconvolution steps
• Zero-pad both block and kernel to extended shape (avoids circular aliasing)
• rfftn(block) and rfftn(kernel) => frequency-domain arrays
• Divide element-wise: S_hat = M_hat / R_hat
• Multiply by Gaussian filter G_hat to suppress high-frequency noise
• irfftn => real-space deconvolved charge
• Roll by kernel half-width to re-center output
• Trim to expected spatial and time extent
3D Gaussian filter
• Separable product of 1D Gaussians along each axis
• Pixel axes: sigma_pixel (in units of pixel pitch)
• Time axis: sigma_time (in same units as adc_hold_delay)
• Built in frequency space via rfftfreq / fftfreq for each axis
• Typical values: sigma_pixel ~ 0.8 pitch, sigma_time ~ 1.6 to several us
Complexity
• FFT-based: O(N log N) where N = total number of voxels
• Compatible with GPU acceleration via PyTorch / CuPy rfftn
• Block-wise deconvolution planned to reduce memory footprint

## Slide 12
Stage 3 — Active Voxel Identification
Selecting reconstructed signal voxels
Algorithm detail
Current strategy
• Gaussian filter applied to deconvolved 3D array
• Voxels with filtered charge > 500 e- are kept as active
• 500 e- corresponds approximately to the LArPix-v2 front-end noise standard deviation
Truth comparison via Gaussian smearing
• The same 3D Gaussian filter is applied to the true ionization charge (from simulation)
• Active deconvolved voxels define a set of (pixel, time-bin) pairs
• True charge in matching pairs is summed and linked to particle ID
• Residual = deconvolved charge - smeared true charge per voxel
• This allows fair comparison without mismatch from detector smearing
Ongoing: Wiener-inspired frequency filter for voxel selection
• Form: F(w) = exp( -(w/a)^b ) applied in frequency domain
• Goal: adaptively suppress noise-dominated frequency bands
• Will replace fixed-threshold selection with a signal-to-noise driven criterion
• Under active development; not yet in the main pipeline
Output payload (NPZ): deconv_q, boffset, smeared_true, smear_offset, hits data, effective-charge truth, template-compensation diagnostics, geometry metadata

## Slide 13
Simulation Setup
How performance is evaluated
Section 3 — performance
Detector and input
• Geometry: ProtoDUNE-ND (2x2 experiment modules)
• Input: positron particle gun
• Simulator: TRED (GPU-accelerated, provides true ionization charge with particle ID)
• Provides: hit data, effective charge truth (effq), waveforms
Metrics
• Charge residual: deconvolved charge minus smeared true charge per active voxel
• Residual width characterizes charge reconstruction resolution
• Studies vary: template choice, filter width, threshold, noise level
Study matrix
Template
center / collection / collection+neighbors / (ongoing: filtered template)
Filter
Pixel Gaussian sigma ~ 0.8 pitch; time sigma from 1.6 us to several us
Threshold
No threshold vs 1000 e- vs 5000 e- (lower threshold preserves more waveform info)
Noise
With and without simulated LArPix-v2 noise (noise is subleading effect)

## Slide 14
Performance Results
What the numbers show
Section 3 — performance
Key result: charge residual width < 500 electrons across evaluated configurations
Templates
Including neighboring-pixel induction (collection_plus_neighbors) improves recovery and reduces ghost hits. Center-only template overestimates charge on induction pixels.
Filters
Pixel-axis Gaussian at sigma ~ 0.8 pitch provides good spatial resolution. Temporal sigma of 1.6 us (one digitization period) preserves timing while suppressing noise.
Threshold
Lower threshold preserves more of the rising waveform and reduces start-time ambiguity. 5000 e- threshold significantly degrades deconvolution quality.
Noise
Noise is a subleading contribution. Waveform truncation and threshold effects dominate reconstruction uncertainty in the current setup.

## Slide 15
Discussion — Truth Bookkeeping
Linking reconstructed charge to simulation truth
Section 4 — discussion
Problem
True ionization charge and deconvolved charge cannot be compared directly because detector smearing affects both. A naive point-by-point comparison would suffer from spatial mismatch.
Solution: apply the same Gaussian smearing to both sides
• TRED saves true ionization charge with particle ID per voxel
• Apply identical 3D Gaussian filter (sigma_pixel, sigma_time) to the true charge
• Define active voxel set from deconvolved output
• Sum smeared true charge within each active (pixel, time-bin) pair
• Link total true charge in each pair to the particle ID with the largest contribution
• Residual = deconvolved charge - smeared true charge per active voxel
This provides a direct bridge between the signal-processing chain and machine-learning-based reconstruction workflows that rely on ionization history tracking.

## Slide 16
Discussion — Hardware & Readout Requirements
What the detector needs to do well
Section 4 — discussion
GPU acceleration (ongoing benchmark)
• FFT deconvolution is O(N log N); scales favorably with detector size
• PyTorch / CuPy rfftn enables GPU offload with minimal code change
• CPU vs GPU benchmark is planned but not yet complete
Readout design recommendations
• Low threshold: preserves rising waveform, reduces start-time ambiguity
• Short burst sequence: limits missing waveform fraction
• Threshold uniformity across pixels is important (todo: quantify)
• Saturation: non-reset during burst means charge can saturate at high topology density
Shield grid study (DUNE internal)
• Ramo theorem: adding a shield grid sharpens the collection-pixel signal
• Suppresses long-range induction on neighboring pixels
• Shorter effective waveform => smaller missing-waveform fraction
• Expected results: cleaner event display, fewer ghost hits, smaller residual width
• Demonstrated using same simulation setup with and without shield grid

## Slide 17
Conclusions
1
Physics-guided waveform recovery via two-pass burst processing (dead-time merge + template compensation)
2
Separate collection and induction templates for pixels with different charge levels (V3)
3
FFT-based 3D deconvolution with integrated field-response kernel and Gaussian filter
4
Charge residual width below 500 electrons demonstrated in simulation
5
Truth bookkeeping framework linking reconstructed charge to simulation particle IDs
Open items
• Wiener-inspired frequency filter for voxel selection (ongoing)
• Block-wise deconvolution for large events (planned)
• CPU vs GPU benchmark (planned)
• Threshold uniformity and saturation studies (planned)
• Shield grid study results (DUNE internal review)